## Slide 1
IAAP
December 5, 2023
Kimberly A. Hoppe Parr, PhD, CIH
GZA GeoEnvironmental, Inc.
Aggregate Miner Safety Conference
Silica Exposure Testing

## Slide 2: Learning Objectives
Background: Silica.
Conducting an exposure assessment.
Evaluate sampling results.
Control exposures.

## Slide 3: What is silica?
IARC 2012
Various types
  Quartz, cristobalite and tridymite.
  Most abundant form is quartz
Silica can occur in crystalline and amorphous forms
Primary commercial product categories
  Sand and gravel
  Quartz crystals
  Diatomites

## Slide 4
  Industrial sand operations
  Sand and gravel aggregate operations
  Limestone aggregate operations
  Slag and concrete recycling operations
  Ready mix concrete operations
  Clean Construction Demolition Debris (CCDD) operations
  Extraction and Processing
Operations That Do or May Involve Silica

## Slide 5: Respirable crystalline silica (RCS)
MSHA and OSHA definition
  Quartz, cristobalite and/or tridymite contained in airborne particles that are determined to be respirable by a sampling device designed to meet the characteristics for respirable-particle size-selective samplers specified in the International Organization for Standardization (ISO) 7708:1995: Air Quality-Particle Size Fraction. (MSHA Proposed Rule and 29 CFR 1910.1053)

## Slide 6
Image: Thakur et al. 2020
Respiratory System
Upper Respiratory:
Oral/nasal cavity
Lower Respiratory:
Trachea/ bronchi
Alveolar region

## Slide 7: Respirable crystalline silica
Respirable- size fraction capable of penetrating to the lower gas exchange region of the lungs.
Image: https://safesilica.eu/respirable-crystalline-silica/

## Slide 8: Lung penetration
Image: https://safesilica.eu/crystalline-silica-the-science/

## Slide 9: Potential Health Outcomes
OSHA 2023
Silicosis
  Incurable lung disease
  Pulmonary scarring (fibrosis).
Lung Cancer
  Increased risk of developing lung cancer.
Chronic Obstructive Pulmonary Disorder (COPD)
Kidney Disease

## Slide 10: Exposure Monitoring
Exposure
Measurable amount
Lung Penetration
Size selective
Deposition
Dose
Health Outcomes

## Slide 11: Occupational Exposure
MSHA
Silica dust is generated in most mining activities
cutting;
sanding;
drilling;
crushing;
grinding;
sawing;
scraping;
jackhammering;
excavating; and
hauling rock, gravel, and sand.
MSHA. Silica Fact Sheet.
Image: Pit and Quarry. 2023

## Slide 12: Evaluate Occupational Exposure to RCS
Exposure
Lung Penetration
Deposition
Health Outcomes

## Slide 13: When to sample?
The employer shall assess the exposure of each employee who is or may reasonably be expected to be exposed to respirable crystalline silica at or above the action level in accordance with either the performance option in paragraph (d)(2)(ii) or the scheduled monitoring option in paragraph (d)(2)(iii) of this section.

## Slide 14: When to sample?
Section 60.12 (a) –
Baseline sampling. The first action mine operators would take to assess miners’ exposures under the proposed rule would be to conduct baseline sampling. Baseline sampling would provide an initial measurement of respirable crystalline silica exposures that would be compared to the proposed action level and the proposed PEL to determine the effectiveness of existing controls and the need for additional controls.
MSHA Proposed Rule

## Slide 15: Initial Determination/ Baseline Sampling
The employer shall perform initial monitoring to assess the 8-hour TWA exposure for each employee
  PBZ
  reflect the exposures of employees on each shift, for each job classification, in each work area.
  Sample similar exposure groups
  Representative sampling

## Slide 16
Planning Field Surveys and Sampling
Where, when, how long, whom, how many
    Personal v. Area
    Full shift v. task based
    Similar exposure groups
Collection method and equipment
Regulatory requirements
Supplemental samples, bulk, and/or field blanks
Identify certified laboratory

## Slide 17: Personal Air Sampling
Air sampling pump
  Calibrate
  Standard methods
    Flow rate
    Duration
Sampling media
  Cyclone
  Parallel particle impactor (PPI)
Images: https://www.sgsgalson.com/silica/

## Slide 18: Particle Size Selective Sampling
Image: SKC
Inhalable (100 μm 50% cut-point)
  upper airways (nose and throat)
Thoracic (10 μm 50% cut-point) -
  Tracheobronchial regions
Respirable (3.5/4 μm 50% cut-point)
  Gas exchange region (alveolar region)

## Slide 19: Air Sampling
Key Steps
  Order equipment
  Calibrate sampling pumps
  Label sampling media
  Record start time
  Document work tasks, breaks, duration each performed
  Record if any personal protective equipment (ppe) was worn
  Record stop time
  Field blanks
  Post-calibrate sampling pumps
  Follow chain of custody procedures to forward samples to a certified laboratory for analysis.

## Slide 20: Air Sampling
Troubleshooting
  Pump stops
    Battery
      Charge overnight prior to sampling
      Bring extra(s) if possible
    Hose blocked or crimped
      Check samplers regularly
  Sampling position
    Breathing zone

## Slide 21: Chain of Custody
Important information
  Date sampled
  Identify the individual who sampled
  Sample ID
  Sample duration or total volume collected
  Analysis requested
  Turn around time
  Date and time submitted to the laboratory

## Slide 22: Analytical Methods
Certified Laboratory
Analytical Methods
  NIOSH 7500/OSHA ID-125; XRD
  NIOSH 7602 and 7603; IR
  MSHA Method P-2 and P-7

## Slide 23: Analytical Results
Sample ID
Volume
Units
Notes or laboratory qualifiers

## Slide 24
Evaluation of Hazards: Occupational Exposure Limits
Occupational Exposure Limits (OELs)
Regulatory
    OSHA
    MSHA
Federal Agency- Research
    NIOSH
Consensus Organizations
    ACGIH

## Slide 25
Occupational Safety and Health Administration (OSHA)
OSHA Permissible Exposure Limits (PEL)
    29 CFR 1910.1000, tables Z-1, Z-2, and Z-3
    Time weighted average (TWA)
      The employee's average airborne exposure concentration in any 8-hour work shift of a 40-hour work week which shall not be exceeded
    Level of exposure established as the highest level of exposure an employee may be exposed to without incurring the risk of adverse health effects.

## Slide 26
OSHA
In 2016 OSHA updated its RCS Standard
Lower PEL and action level for RCS exposures
    OSHA PEL for RCS = 50 μg/m3
    OSHA Action Level for RCS = 25 μg/m3
Applicable to general industry, construction, and maritime
Additional requirements included:
    Construction (1926.1153)
    General Industry and maritime (1910.1053)

## Slide 27
Mine Safety and Health Administration (MSHA)
For MNM mines,
  The existing exposure limit for quartz is 100 μg/m3 for a full-shift exposure, calculated as an 8-hour TWA.
For coal mines,
  There is no separate standard for RCS.
  Regulated through reductions in the overall respirable coal mine dust standard.
Limit miners’ exposures to RCS using
    Engineering controls as the primary means of suppressing, diluting, or diverting dust generated by mining activities.

## Slide 28
MSHA- Proposed Standard
MSHA- Silica Fact Sheet
Lower PEL and action level for RCS exposures
    MSHA PEL for RCS = 50 μg/m3
    MSHA Action Level for RCS = 25 μg/m3
Medical surveillance
    MNM and coal miners
    Early detection
Respiratory protection
    ASTM 2019- “Standard Practice for Respiratory Protection,”

## Slide 29
NIOSH
Non-Regulatory Occupational Exposure Limits
National Institute for Occupational Safety and Health (NIOSH)
  NIOSH Recommended Exposure Limits (RELs)
    10 hour work day, 40 hour work week
  NIOSH REL for RCS = 50 ug/m3

## Slide 30
ACGIH
American Conference of Governmental Industrial Hygienists
  ACGIH Threshold Limit Values (TLV)
    8-hour Time Weighted Average (TWA)
    Airborne concentration which most workers can be repeatedly exposed during an eight-hour work day over a working lifetime and experience no adverse health effects
    ACGIH TLV for RCS = 25 ug/m3

## Slide 31: Occupational Exposure Limits
Agency/Group | Standard
OSHA | 50 μg/m3
MSHA (existing) | 100 μg/m3
MSHA (proposed) | 50 μg/m3
NIOSH | 50 μg/m3
ACGIH | 25 μg/m3

## Slide 32
Evaluation of Hazards: Occupational Exposure Limits
Compare sampling results to the Occupational Exposure Limits
Calculate a Time Weighted Average
TWA = (C1T1) + (C2T2 ) …+ (CnTn)
Total Time (8 hours)

## Slide 33
EXAMPLE: TWA Calculation
Calculation of an 8-hour TWA
  1 hours at 200 µg/m3
  5 hours at 0.1 µg/m3
  2 hours at 0 µg/m3
Did we exceed the PEL for RCS?

## Slide 34
EXAMPLE: TWA Calculation
TWA = (C1T1) + (C2T2 ) …+ (CnTn)
Total Time (8 hours)
TWA = (1 hr x 200 µg/m3) + (5 x 0.1 µg/m3 ) + (2 x 0)
8 hours
TWA = (200) + (0.5)+(0)
8 hours
    TWA = 25.1 µg/m3
  1 hours at 200 µg/m3
  5 hours at 0.1 µg/m3
  2 hours at 0 µg/m3
RCS
OSHA PEL = 50 µg/m3
MSHA PEL = 100 µg/m3 **
**MSHA Proposed PEL = 50 µg/m3

## Slide 35: Occupational Exposure Limits
PEL (Permissible Exposure Limit)
Regulatory Limit set by OSHA and MSHA
REL (Recommended Exposure Limit)
Recommended limit set by NIOSH
TLV (Threshold Limit Value)
Recommended limit set by ACGIH
Action Level

## Slide 36: Action Level and PEL
Below the Action Level
  employer may discontinue monitoring for those employees whose exposures are represented by such monitoring.
Above the action level but at or below the PEL,
  the employer shall repeat such monitoring within six months of the most recent monitoring.
Exceeding the PEL
  the employer shall repeat such monitoring within three months of the most recent monitoring

## Slide 37
Employee Notification
Informing Workers
  Inform workers about sampling and rationale.
  OSHA requires that results indicating over exposure be
  communicated to workers, ethical to provide all data.

## Slide 38: Evaluate Occupational Exposure to RCS- Control Exposures
Exposure
Lung Penetration
Deposition
Health Outcomes

## Slide 39
Control of Occupational Hazards

## Slide 40
Evaluation of Hazards: Occupational Exposure Limits
Time
(minutes)
Concentration/ Level
STEL/ Ceiling
limit
8-hr TWA
Real-time sampling
480

## Slide 41
Identify specific tasks where exposure(s) may occur
  If employee does not interact with silica regularly
Task-Based Sampling
If you exceed action level/PEL
  Aid in identifying major contributing factors to overall TWA

## Slide 42
Task based
Test
- Short term sampling
- Focus on a specific task or operation
Real time monitoring
- Immediate results
- Measure peak exposure(s)
Evaluate
- Recommend controls or work requirements
Task-Based Monitoring

## Slide 43
Control of Hazards
Evaluate Control Effectiveness
Periodic testing of ventilation systems,
local exhaust.
Sampling after the implementation of engineering controls.
Inspection, cleaning and maintenance of PPE.
Review of administrative programs annually.

## Slide 44
Reassessment of Exposures
Change in the
    production,
    process,
    control equipment,
    personnel, or
    work practices
  That may reasonably be expected to result in new or additional exposures at or above the action level, or
When the employer has any reason to believe that new or additional exposures at or above the action level have occurred.

## Slide 45
Notice of Proposed Rule Making
Update to the MSHA silica standard
  July 13, 2023
  Permissible Exposure Limit to respirable crystalline silica at or below 50 µg/m3 for a full shift exposure, calculated as an 8-hour time weighted average.
  Update to other components of the standard
  Improve Respiratory Protection
Comment Period closed September 11, 2023
Notes: Tomorrow’s Presentation:10:30-11:15 MSHA's New Silica Rule, presented by Nick Scala (Conn Maciel Carey, Chair MSHA Workplace Safety Group)

## Slide 46
Thank you!
Kimberly A. Hoppe Parr, PhD, CIH
Senior Project Manager
Occupational and Environmental Health Scientist/ Toxicologist
GZA GeoEnvironmental, Inc.
17975 West Sarah Lane, Brookfield, WI 53045
(262)754-2584
kimberly.parr@gza.com