## Slide 1: MSHA’s Proposed Silica Rule
IAAP Annual Meeting and Convention
December 6, 2023
Nicholas “Nick” W. Scala
Chair of Conn Maciel Carey’s MSHA • Workplace Safety Group

## Slide 2: Nicholas W. Scala nscala@connmaciel.com • 614.418.6048
Nick Scala is a Chair of the national MSHA • Workplace Safety Practice at Conn Maciel Carey LLP and a Certified Mine Safety Professional. He focuses on all aspects of mine safety and health law:
  Represents mine operators and independent contractors in inspections, investigations & enforcement actions involving MSHA
  Advises clients in all phases of involvement with MSHA, particularly guiding companies through contest proceedings before the Federal Mine Safety and Health Review Commission
  Prepares clients for and manages incident, fatality, and special investigations conducted by MSHA, and defends company representatives in section 110 proceedings, and represents companies in discriminations/interference investigations and proceedings

## Slide 3: MSHA’s Proposed Rule Status

## Slide 4: MSHA’s Proposed Rule Status
THE RULE IS NOT YET FINAL
THE RULE IS NOT YET EFFECTIVE
THE RULE IS NOT YET ENFORCEABLE
MSHA INSPECTORS CANNOT REQUIRE YOU TO COMPLY WITH PROVISIONS OF THE PROPOSED RULE

## Slide 5: MSHA’s Proposed Rule Status
MSHA’s Respirable Crystalline Silica rule is formally titled:
  Lowering Miners' Exposure to Respirable Crystalline Silica and Improving Respiratory Protection
It was published in the Federal Register on July 13, 2023
  Comment deadline was originally 45-days after the publishing date
  MSHA extended the comment period for 15-days, ending September 11, 2023
MSHA held 3 in-person hearings during this time
  Arlington, VA
  Beaver, WV
  Denver, CO
The comment period is now closed. MSHA is reviewing and responding to comments, and potentially revising the proposed rule.

## Slide 6: MSHA’s Proposed Rule Status
Likely, the next step will be for MSHA to submit its final version of the rule to the White House’s Office of Management and Budget (OMB). The comment period could be reopened, but that is seen as unlikely.
The rule will be reviewed, and either approved to be published as Final in the federal register or sent back to MSHA for further revision.
In the proposal, MSHA stated an effective date of 120-days (approximately 4 months) after the final rule is published in the federal register.
  Numerous industry associations and individual stakeholders pushed back seeking a more significant grace period to get into compliance with the requirements of the final rule.
It is expected that MSHA is doing all it can to finalize this rule and have the final rule published in 2024, possibly as early as Spring or early Summer.

## Slide 7: Existing MSHA Regulation of Silica

## Slide 8: Existing MSHA Standards
Current MSHA Permissible Exposure Limit – 100 µg/m³
  Incorporated by reference of Threshold Limit Values for Chemical Substances in Workroom Air Adopted by ACGIH for 1973
Testing Requirements: 30 CFR 56/57.5002
  Dust, gas, mist, and fume surveys shall be conducted as frequently as necessary to determine the adequacy of control measures.
Respiratory Protection Program incorporated by Reference ANSI Z88.2-1969

## Slide 9: Existing MSHA Enforcement Initiative
MSHA Silica Enforcement Initiative
  Rolled out in 2022 with several other MSHA safety initiatives
  MSHA is implementing a Silica Enforcement Initiative to protect Coal and Metal and Nonmetal (MNM) miners’ health by limiting their exposures to respirable crystalline silica. This initiative has four components: inspections, sampling, compliance assistance, and miners’ rights.
  Inspections Coal and MNM mines
  MSHA will conduct spot inspections for silica at coal and MNM mines.
    At mines with repeated overexposures to silica.
    This will include, where warranted, inspections in accordance with Section 103(i) of the Mine Act.
    MSHA will require for overexposures over 100 micrograms per cubic meter (existing PEL):
      For MNM mines, abatement within a period of time.
        For overexposures not abated, MSHA will issue a 104(b) withdrawal order.
      For coal mines, MSHA will encourage mine operators to change the dust control and mine ventilation plans and review plans/exposures after changes are made.
Notes: Miners’ Voice
MSHA will reinvigorate efforts to educate miners about their rights to make hazardous condition complaints and their protections against retaliation and discrimination.
MSHA will ensure that miners are aware of their right to:
  Accompany an MSHA inspector.
  Obtain an immediate MSHA inspection if they believe safety or health hazards exists.
  Identify hazardous conditions and refuse unsafe work without fear of retaliation and discrimination.
  Additional information will be posted on the MSHA’s website.
  Compliance assistance materials will be provided through the Educational Field and Small Mine Services staff.

## Slide 10: Existing MSHA Enforcement Initiative
MSHA Silica Enforcement Initiative
  Miners’ Voice
    MSHA will reinvigorate efforts to educate miners about their rights to make hazardous condition complaints and their protections against retaliation and discrimination.
    MSHA will ensure that miners are aware of their right to:
      Accompany an MSHA inspector.
      Obtain an immediate MSHA inspection if they believe safety or health hazards exists.
      Identify hazardous conditions and refuse unsafe work without fear of retaliation and discrimination.
      Additional information will be posted on the MSHA’s website.
      Compliance assistance materials will be provided through the Educational Field and Small Mine Services staff.
Notes: Miners’ Voice
MSHA will reinvigorate efforts to educate miners about their rights to make hazardous condition complaints and their protections against retaliation and discrimination.
MSHA will ensure that miners are aware of their right to:
  Accompany an MSHA inspector.
  Obtain an immediate MSHA inspection if they believe safety or health hazards exists.
  Identify hazardous conditions and refuse unsafe work without fear of retaliation and discrimination.
  Additional information will be posted on the MSHA’s website.
  Compliance assistance materials will be provided through the Educational Field and Small Mine Services staff.

## Slide 11: MSHA’s Proposed Rule

## Slide 12: MSHA’s Proposed Rule for RCS
Lowering Miners’ Exposure to Respirable Crystalline Silica and Improving Respiratory Protection
Proposes creation of new part in 30 CFR, Part 60 - Uniform Mine Health Regulations (subpart M)
Part 60 – Respirable Crystalline Silica
  60.1 Scope; effective date.
  60.2 Definitions.
  60.10 Permissible Exposure Limit (PEL).
  60.11 Methods of compliance.
  60.12 Exposure monitoring.
  60.13 Corrective actions.
  60.14 Respiratory protection.
  60.15 Medical surveillance for metal and nonmetal miners.
  60.16 Recordkeeping requirements.
  60.17 Severability.

## Slide 13: Proposed Changes
§60.10 – Permissible Exposure Level (PEL)
  The mine operator shall ensure that no miner is exposed to an airborne concentration of respirable crystalline silica in excess of 50μg/m³ for a full-shift exposure, calculated as an 8-hour TWA.
§60.2 – Definitions:
  Action Level: means an airborne concentration of respirable crystalline silica of 25 micrograms per cubic meter of air (μg/m³) for a full-shift exposure, calculated as an 8-hour time weighted average (TWA).
§60.11 – Methods of Compliance:
  (a) The mine operator shall install, use, and maintain feasible engineering controls, supplemented by administrative controls when necessary, to keep each miner's exposure at or below the PEL, except as specified in § 60.14.
  (b) Rotation of miners shall not be considered an acceptable administrative control used for compliance with this part.
Notes: §60.1 – Scope and effective date:
  New rule will apply to Metal/Nonmetal and Coal mines
  Set to be effective 120 days post publication of final rule
    This has not happened to date
    The provisions of this rule are not yet in effect
    MSHA cannot enforce the provisions contained within this Proposed Rule

## Slide 14: Compliance Methods
§60.11 – Methods of Compliance:
  (a) The mine operator shall install, use, and maintain feasible engineering controls, supplemented by administrative controls when necessary, to keep each miner's exposure at or below the PEL, except as specified in § 60.14.
  (b) Rotation of miners shall not be considered an acceptable administrative control used for compliance with this part.
Engineering controls are prioritized over administrative controls, including use of respiratory protection.
  Examples provided by MSHA include ventilation systems, dust suppression, enclosed cabs with filtered breathing air, water sprays, etc.
  This is consistent with what MSHA’s approach the last few years when overexposures are identified
  Places burden on operators to update equipment and/or processes to bring RCS exposure below PEL and Action Level (AL)
Administrative controls are stated as a supplement to engineering. MSHA identifies the following as administrative controls, housekeeping, work positions, cleaning of spills, and measure to prevent contamination of clothing.

## Slide 15: Monitoring/Testing

## Slide 16
SAMPLING REQUIREMENTS
Sample during “typical mining activities”
Representative sampling: 2+ miners doing same task, same shift, same work area
Full-shift sample; time weighted average
Breathing zone air samples
Post sampling results 31 days; retain 2 years
Baseline Sampling (within 180 days of rule)
<25
25-50
>50
Verify:
Prior 12 months of data
Objective data
Re-sample w/in 3 months
Qualitative Evaluation
Every 6 months (+create record; post for 31 days)
Periodic Sampling every 3 months
Corrective Actions
Corrective Action Sample
<25
No changes that will expose miners >25
Two tests in a row <25
Changes that may expose miners >25
Post-evaluation sample
<25
???
Sample Analysis:
ISO/IEC 17025 accredited labs
Methods:
  MSHA P-2
  NIOSH 7500
  OSHA ID-142

## Slide 17: Exposure Monitoring
§60.12 – Exposure Monitoring:
  The proposal requires both monitoring by means of sampling, what MSHA refers to as quantitative, and periodic evaluation of process and controls measure, or qualitative
§60.12(a) – Baseline Monitoring:
  Mine operator shall perform within 180 days (6 months) of effective date, sampling for each miner who is or may reasonably be expected to be exposed to RCS.
    May reasonably be expected – MSHA assumes this includes all miners in processing and extraction
  Can use representative sampling for miners performing the same task, on the same shift, in the same work area. (§60.12(f)(3))
  If baseline monitoring comes back below 25μg/m³, operator must verify this by:
    MSHA or operator sampling data in last 12 months (from time of sample)
    Another sample taken within 3-months
    Objective Data
Notes: “Representative fraction” = 2+ miners doing same task, on same shift, in same work area and expected to have highest exposure (p 183)
Objective data means information, such as air monitoring data from industry-wide
surveys or calculations based on the composition of a substance, demonstrating miner exposure
to respirable crystalline silica associated with a particular product or material or a specific
process, task, or activity. The data must reflect mining conditions closely resembling or with a
higher exposure potential than the processes, types of material, control methods, work practices,
and environmental conditions in the operator's current operations.

## Slide 18: Exposure Monitoring
§60.12(b) – Periodic Monitoring:
  If data from baseline monitoring (or collected at a later date) comes back with miners exposed at levels greater than the AL (25μg/m³) but below the PEL (50μg/m³), operators need to conduct further monitoring
    Completed within 3 months of prior sample
    Completed until there are two consecutive samples collected below the AL (25μg/m³)
§60.12(c) – Corrective Action Sampling:
  In the event samples come back greater than the PEL (50μg/m³) then operator is required to implement corrective actions and sample until result come back at or below the PEL, and then per Periodic Monitoring
    Additional requirements for Corrective Actions includes in §60.13
Notes: “Representative fraction” = 2+ miners doing same task, on same shift, in same work area and expected to have highest exposure (p 183)
Objective data means information, such as air monitoring data from industry-wide
surveys or calculations based on the composition of a substance, demonstrating miner exposure
to respirable crystalline silica associated with a particular product or material or a specific
process, task, or activity. The data must reflect mining conditions closely resembling or with a
higher exposure potential than the processes, types of material, control methods, work practices,
and environmental conditions in the operator's current operations.

## Slide 19: Evaluation and Monitoring
§60.12(d) – Semi-Annual Evaluation:
  Operators shall evaluate any changes in production, processes, engineering or administrative controls, or other factors that may reasonably be expected to result in new or increased respirable crystalline silica exposures. Once the evaluation is completed, the mine operator shall:
    (1) Make a record of the evaluation and the date of the evaluation; and
    (2) Post the record on the mine bulletin board and, if applicable, by electronic means, for the next 31 days.
  Required to take place at least every 6-months
  Begins 1-year after effective date of rule
§60.12(e) – Post-Evaluation Sampling:
  If operator determines miners may be exposed to RCS at or above the AL (25μg/m³), operators must conduct sampling for each miner who is or may reasonably be expected to be exposed at or above AL

## Slide 20: Sample Collection and Records
Additional Sampling Requirements:
  Samples are conducted for 8-hour time weighted average
  Must be in the breathing zone of miner
  Must use sampling equipment that conform to ISO 7708:1995 requirements
  Must use ISO/IEC 17025 Accredited Labs for analysis
  Must ensure labs use proper methods outlined by MSHA, NIOSH, or OSHA
§60.12(h) – Sampling Records:
  Records must include, date, sampled occupation, results for RCS and respirable dust exposure level
  Records must be maintained for at least 2 years by operator
  Records must be posted – including the lab report – for 31 days.
    Posting either electronically, physically, or both
Notes:   X-ray diffraction (XRD) methods (MNM):
    MSHA P-2
    NIOSH 7500
    OSHA ID-142

## Slide 21: Recordkeeping
§60.16(a)
§60.16(b) Upon request from an authorized representative of the Secretary, from an authorized representative of miners, or from miners, mine operators shall promptly provide access to any record listed in this section.
Notes:   X-ray diffraction (XRD) methods (MNM):
    MSHA P-2
    NIOSH 7500
    OSHA ID-142

## Slide 22: Corrective Action, PPE, and Surveillance

## Slide 23: Corrective Action & PPE
§60.13 – Corrective Actions:
  If sampling results are greater than the PEL (50μg/m³), operator must implement corrective actions
  (2) Ensure that affected miners wear respirators properly for the full shift or during the period of overexposure until miner exposures are at or below the PEL; and
  (3) Immediately take corrective actions to lower the concentration of respirable crystalline silica to at or below the PEL.
  (4) Once corrective actions have been taken, the mine operator shall:
  (i) Conduct sampling pursuant to § 60.12(c); and
  (ii) Take additional or new corrective actions until sampling indicates miner exposures are at or below the PEL.
  Operator must document the corrective actions taken, and maintain record of the corrective actions for 2-years, providing them to MSHA upon request

## Slide 24: Corrective Action & PPE
§60.14 – Respiratory Protection:
  Only permitted for temporary use if:
    (1) Engineering control measures are being developed and implemented; or
    (2) It is necessary by the nature of work involved.
  Respirators must be protection classified as 100 series (i.e. no more N95)
  Respiratory Protection Program compliant with ASTM F3387-19 must be implemented
§60.14(b) Miners unable to wear respirators. Upon written determination by a physician or other licensed health care professional (PLHCP) that an affected miner is unable to wear a respirator, the miner shall be temporarily transferred either to work in a separate area of the same mine or to an occupation at the same mine where respiratory protection is not required.
  The affected miner shall continue to receive compensation at no less than the regular rate of pay in the occupation
  held by that miner immediately prior to the transfer.
  (2) The affected miner may be transferred back to the miner’s initial work area or occupation when temporary non-routine use of respirators under paragraph (a) of this section is no longer required.
Notes: (c) Respiratory protection requirements. (1) Affected miners shall be provided with a
NIOSH-approved atmosphere-supplying respirator or NIOSH-approved air-purifying respirator
equipped with the following:
(i) Particulate protection classified as 100 series under 42 CFR part 84; or
(ii) Particulate protection classified as High Efficiency “HE” under 42 CFR part 84.
(2) Approved respirators shall be selected, fitted, used, and maintained in accordance

## Slide 25: Medical Surveillance
§60.15 – Medical Surveillance
  Metal/Nonmetal operators shall provide to each miner periodic medical examination to include;
    Medical/work history
    Physical exam (emphasis on respiratory)
    Chest X-ray
    Pulmonary function test
  Medical examination must be offered at least every 5 years
    It is not required for miners to participate in this examination, However…
§60.15(c): Every new miner must receive medical examination within 30-days of employment, a follow-up within 3 years, and follow-up with specialist within 2-years if the follow-up show evidence of decreased lung function
§60.15(e): Written medical opinion
  The mine operator shall obtain a written medical opinion from the PLHCP or specialist within 30 days of the medical examination. The written opinion shall contain only the following:
(1) The date of the medical examination;
(2) A statement that the examination has met the requirements of this section; and
(3) Any recommended limitations on the miner’s use of respirators.
Notes: Each operator of a metal and nonmetal mine shall provide to
each miner periodic medical examinations performed by a physician or other licensed health care
professional (PLHCP) or specialist, as defined in § 60.2, at no cost to the miner.
administered by a spirometry
technician with a current certificate from a NIOSH-approved Spirometry Program Sponsor.
specialist =
  “an American Board-Certified Specialist in Pulmonary Disease or an American Board-Certified Specialist in Occupational Medicine.” (p 163)
  Physician or other licensed health care professional" (PLHCP)

## Slide 26: Possible Changes…

## Slide 27: Part 90 for M/NM Mines?
MSHA sought comment on inclusion of a Part 90-esque provision for M/NM
  Request for Comment #36
  MSHA requests comments as to whether the proposed provisions should include a medical removal option for MNM miners who have developed evidence of silica-related disease that is equivalent to the transfer rights and exposure monitoring provided to coal miners in 30 CFR part 90 (Part 90).
  Under Part 90, any coal miner who has evidence of the development of pneumoconiosis based on a chest X-ray or other medical examinations has the option to work in an area of the mine where the average concentration of respirable dust in the mine atmosphere during each shift to which that miner is exposed is continuously maintained at or below the applicable standard. Under Part 90, coal miners are entitled to retention of pay rate, future actual wage increases, and future work assignment, shift and respirable dust protection. MSHA seeks comment on whether this medical removal option should be provided to MNM miners.

## Slide 28: Self-Reporting and Enforcement
During the August 21, 2023, public hearing held in Denver, CO, remarks were made that a potential significant and novel expansion on the language of the proposed rule was under consideration. In MSHA’s opening remarks, MSHA Deputy Assistant for Operations Patricia Silvery stated:
“Further, if an operator's sample is above the proposed PEL, the mine operator would be required to take immediate corrective actions to reduce miners' exposure to below the PEL, make the record of the overexposure which would have to be posted and made available to miners' representatives and re-sampled to ensure that the corrective action is effective and that miners' exposures are, in fact, reduced to at or below the PEL. And if the miners' exposures exceed the PEL, MSHA would issue a citation. MSHA has received comment on the recordkeeping requirement.
Some commenters recommend that exposure records be kept for longer than two years. At this point in the rulemaking process, MSHA is considering to require that when an operator's sample is over the PEL, that operator send the record of that overexposure to the MSHA district manager. This exposure data will allow MSHA to immediately take appropriate enforcement action and provide any necessary compliance assistance to operators.”
MSHA’s Denver Public Hearing Transcript, page 9, lines 6-11 (August 21, 2023)

## Slide 29: Questions?

## Slide 30: Contact Information
Nick Scala
Chair, MSHA • Workplace Safety Group
Conn Maciel Carey LLP
614.418.6048
nscala@connmaciel.com
@MSHA_Guy (Twitter)

## Slide 32: Check Out Our Blogs